## Slide 1
Florida Geological Survey
Using QGIS to Generate Web-Ready
3D Visualizations
Seth Willis Bassett, GISP
Levi M. Hannon
Katherine M. White
Florida Geological Survey
Florida Department of Environmental Protection

## Slide 2: Who are we?

## Slide 3: Florida’s STATEMAP

## Slide 4
How do we generate and share 3D content easily?
How do we take STATEMAP and FGS geologic data to the next level and remain competitive?
Motivations

## Slide 5: Solutions
ArcScene
  Pros:
    Available to most GIS analysts
  Cons:
    Low quality 3D visualizations
    Only ‘web ready’ format is VRML
      Originally Specified 1994
      Superseded by X3D in 2004

## Slide 6: Solutions
ArcGIS Pro
  Pros:
    Available to most GIS analysts
    Integration of 2D and 3D visualization
    Web Ready Exports to ArcGIS Online
  Cons:
    Buggy
    Only positive z-values are supported

## Slide 7: Solutions
QGIS
  Pros:
    100% free
    Can generate web-ready content using plugins
    Mobile compatible
  Cons:
    Limited resolution
    Good data preparation is essential

## Slide 8: Software Stack
ArcGIS 10.2.2 (Preparation)
QGIS 2.10.1 Pisa
Minoru Akaqi’s Qgis2threejs plugin (v1.4)
WebGL
three.js

## Slide 9: WebGL Compatibility
Link to Source

## Slide 10: Data Preparation: Rasters
QGIS Requires:
  Single Band .tif elevation raster
  Optional RGB image to drape over elevations
  Additional Raster Surfaces

## Slide 11: Data Preparation: Rasters

## Slide 12: Data Preparation: Rasters

## Slide 13: Data Preparation: Rasters

## Slide 14: Data Preparation: Rasters

## Slide 15: Data Preparation: Rasters

## Slide 16: Data Preparation: Rasters

## Slide 17: Gotchas: Setting Null Values

## Slide 18: Gotchas: Setting Null Values

## Slide 19: Gotchas: Setting Null Values

## Slide 20: Gotchas: Set Nulls = -1

## Slide 21: Gotchas: Set Nulls = -1

## Slide 22: Data Preparation: Vector
Considerations:
  What will your 3D visualization look like?
  What features and Z values are required for your 3D visualization?
  Are elevations stored as relative (LSE) or absolute (MSL)?
  Are Z values stored as attributes or z-values?
SHP Specific Considerations:
  How do I handle NULL values?
  Are the first 9 characters of each column interpretable?

## Slide 23: Data Preparation: Vector
Borehole Data: ArcGIS
Target: 3D Cylinders
Attributes for:
  Surficial Elevation (LSE)
  Depth to top of unit
No Z-values
NULL stored as NULL

## Slide 24: Data Preparation: Vector
Borehole Data: QGIS
Target: 3D Cylinders
Each unit now has:
  NEGATIVE elevation (LSE)
  POSTIVE depth to next unit (height)
NULL stored as 999

## Slide 25: Katherine White
3D Borehole Visualization

## Slide 26: Florida Geological Survey
Boreholes
  Wells drilled by FGS drillers
Core Samples
  Analyzed by FGS Geologists
Notes: Shram

## Slide 27: 3D Borehole- QGIS Layout
Notes: Layer Order?

## Slide 28: 3D Borehole- Surficial Geology
Notes: Pan sharpened layer in ARC and North Arrow added by Inkscape

## Slide 29: 3D Borehole- Exporting to three.js
Notes: Broke out wells according to individual formations by excluding nulls

## Slide 30: 3D Borehole- Exporting to three.js
Notes: Broke out wells according to individual formations by excluding nulls

## Slide 31: Levi Hannon
3D Surface Generation

## Slide 32: 3D Surface Generation
Predicted surface models built in Arc
Contours built in Arc
Z-values are relative MSL
Editing attribute tables is simple in QGIS
Overall export to Three.js is quick and easy to replicate
  QGIS saves the previous export options
  Option to save all setting as plain text json file

## Slide 33: 3D Surface Generation

## Slide 34: 3D Surface Generation

## Slide 35: 3D Surface Generation
Exports plain text JavaScript. Layer order can be changed with cut/paste

## Slide 36: 3D Surface Generation - Issues
Preparation of data in Arc to make “pretty” image
  Masking to boundary to eliminate false barrier (“sandbox” effect)
  Extents of surfaces differ based on data extent
    Different extents do not play nice in Three.js
Raster images have to be resampled
  Reduce resolution of LIDAR
Color ramps are a nice idea…..
  ….but there is no easy way to edit saved ramps without starting from scratch

## Slide 37: 3D Surface Generation - Issues

## Slide 38: 3D Surface Generation - Issues

## Slide 39: Wrapping for Web Presentation
Notepad++ and CTRL-F to brand three.js visualizations with FGS and STATEMAP links
Wrapped project and presentation info into an RMarkdown document
Bonus Visualizations
Committed to github repository (gh_pages branch)
http://floridageologicalsurvey.github.io/SHRUG2015

## Slide 40: The Good
Free
Simple
Straight forward
Easy to share
  Easy to use in html platform
  Supported by Firefox, Google Chrome and internet Explorer 11
Quick layer manipulation
Create multiple visualizations quickly and easily

## Slide 41: The Bad
Not easily customizable without knowledge of javascript
“What you get is what you get…”
Struggles with large files
  Can’t throw the “kitchen sink” at it
Data needs to be “neat” before inputting into the three.js plugin
Unexplained drawing failures

## Slide 42: The Ugly
North Arrow and scale bar have to be photo-shopped and “creatively” generated in Arc for Three.js
Labeling
Attribute tables export as is
  Unable to display only ‘desirable’ attributes
Analysis is limited to visualization
  Limited visualization techniques in Three.js

## Slide 43: Final Evaluation
Recommended for easy sharing of 3D visuals, esp for non tech individuals or those that lack ArcGIS software..
“Gee whiz” Visuals
Difficult to incorporate standard map elements like scale and north arrows
Might require image editing software and skills
Fairly clean open source product with minimal learning curve

## Slide 44: Last Word
Is three.js suitable for professional visualization or is it just a toy?
Seth: Yes, if you are comfortable with clean data preparation and troubleshooting open source problems
Katie: Yes.
Levi: Yes, as a visualization tool. No for analysis